## Slide 1: Chase lab data pipeline
Hiroo Miyata

## Slide 2
Sorting
Connect to chase lab data server
By WinSCP
Download files
delayedCOut.plx or nev/
TaskData folder/ ns4 data
Export .nex file
Do check off export unsorted spike timestamps. Do not check any of the others
Import .nev file
Change directory to Rocky/XXXXAdam_2022/Blackrock_anterior/
Save sorted data into .plx
Export .plx file
Spike sorting
Sorting Techniques (Only for me Hiroo)
Check peak-valley vs PC2. two-head shape is likely to have neurons。各場所ごとのwaveformを確認して、spikeっぽいところをadd unitする
PC2, PC1も明らかに分離していることが多いので、PC2 vs PC1も必ず見ること
そして時々PC3に重要なNeuron が隠れていることもあるので、PC3 vs PC2も必ず見ること
次に、境界線はどこら辺かを調べるのが大事。最初は細かくadd unitを行い、それらのcross correlationを確認する。その形から、どの神経集団が同じクラスターに存在するのか大体検討がつく。
次に、ノイズデータの除去をする。ISI=0にノイズデータがあった場合、PC1vsPC2でノイズの中心に近い神経データを除去する。スパイクの形に応じてPeak vs PC1 or PC2 もしくはValley vs PC1 or PC2を確認し、下限値を削除してあげると解決することがある。この時、事前にかく場所のwaveformを確認して、自分のremove wfが妥当かどうかを確認しておいたほうがいい。
最後に、Timestampを見る癖をつけたほうがいい。神経が動いたことにより取れる神経データが変化していないか、確認するべし。時々すごい変化して最初と最後で別のスパイクに見えることがあるので、TimeStampは要注意
大体スパイクが15000あると安心10000以下は基本ダメ
Unitの順序はそろえる。そうすることで後で見やすくなる
Export .txt file
Export Per-Unit Data/All Channels into one file/export fields are Channel and Unit Number/“Append Template Waveform Data in units of” and not “Template Std Dev Data”

## Slide 3
After sorting
synchRockyDataToTask
Make synchInterim data
RockyDataPreprocessing
Make preprocessed datas
CombineTrialData
Make own dataset based on ones interest
Find bad trials
(fullTrialSpikeRateMat) < minSpikeRate
remove "outlier trials“
Template
pp_spikeAlignmentToTrial
Find bad units
mean(fullTrialSpikeRateMat,2) < minSpikeRate;
lowVarUnits = std(fullTrialSpikeRateMat,[],2) < minSpikeRate
Remove >75% increase or drop in FR
the channel just goes crazy and gets ridiculously high values
Remove duplicated "cross-talk" units
Separate data into trials : pp_preprocessTaskAndKinematicData
Align hand data : pp_preprocessTaskAndKinematicData
Align Spike data : pp_spikeAlignmentToTrial + p1_spikePreprocessing
Align EMG/ECG data : pp_emgPreprocess + pp_emgNormalization
Align Pupil data : pp_pupilPreprocess
RockyDataPreprocessing

## Slide 4
Unit Identification
convert dataset each day to dataset across day
Check max FR difference allowed
Template
Convert data format from Chase Lab’s to Batista Lab’s
UnitDScriptForHiroo.m
Calculate mean firing rate, spike train, mean waveform
unitIdentification.m
Calculate correlations, wavescore, autoscore, basescore.
CorrScore : cross-correlograms between this neuron and every other neuron
Wavescore : The correlation of normalized
Autoscore : Inter-spike-interval (ISI) autocorrelation
Basescore : Daily change of log( length(spiketimes) / {max(FR) –min(FR)} )
Calculate survival and corrscore.
Find same channel and unit data,
Get corrscore : computeCorrScore
Update survival by 10 times computeSurvival
Calculate survival
Use wavescore, autoscore, basescore, corrscore
Get possibility if the units are the same
Update survival based on threshold (99%)
IterateSurvival.m
ComputeSurvival.m
Change the unitID to root unitID
p2_v3_unitIdentification_withSkips.m
p2b_chronicUnitTCs.m
Get the direction label and the spike train
in each trials and each unique units